## Slide 1
Optical Design of PICO, a Concept for a Space Mission to Probe Inflation and Cosmic Origins
K. Young1†, M. Alverez, N. Battaglia2, J. Bock, J. Borrill4, D. Chuss5, B. Crill3, J. Delabrouille6, M. Devlin7, L. Fissel8, R. Flauger9, D. Green, K. Gorski, S. Hanany1, R. Hills, J. Hubmayr, B. Johnson, B. Jones2, L. Knox10, A. Kogut11, C. Lawrence3, T. Matsumura, J. McGuire, J. McMahon12, R. O’Brient, C. Pryke1, X.Z. Tan1, A. Trangsrud3, Q. Wen1, G. de Zotti20
image?
Scientific Objectives
Detect or place limits on the energy scale of inflation
Determine the number of light relic particles, Neff
Constrain Σmν, the sum of neutrino masses to 15 meV
Measure τ, the Thompson scattering optical depth to reionization to cosmic variance limits
Understand the role of Galactic magnetic fields in star formation and galactic evolution
… clusters, infrared galaxies, SZ effect, … ? background
Satellite and Instrument
70 times the polarization sensitivity of Planck
21 bands from 20 GHz to 800 GHz
12,996 polarization sensitive TES bolometers
1’ resolution at 800 GHz, 38’ at 20 GHz
Full-sky coverage
TDM readout: 128 rows, 100 columns
Launch vehicle is a Falcon 9, 4.6 meter fairing
Precession and spin based scan strategy from L2 with α = 26°, β = 69° ??
Noise Assumptions
Mirrors at 40K, 4K, emissivity,
Active cooling of stop and secondary
Stop at 4K
FDM/TDM readout system, > x100 multiplexing
Lens coupled broadband multichroic pixels
100 mK bath
Psat = 2x Pload
4 year mission at 95 % observing efficiency
Orbit at L2
White noise: photon, phonon, readout, Johnson
Details. . . .
Optical Design
1.4 m Open Dragone, numerically optimized]
19 x 13 degree field of view
f/1.42 system gives compact focal plane
Focal Plane
50 cm
Focal Plane,
100 mK
Secondary,
10 K
Aperture Stop, 6 K
Primary, 15 K
Alternative Design Considered
Pixel Type | Upper Frequency (GHz) | Number
A | 48.6 | 68
B | 58.3 | 108
C | 145 | 360
D | 174 | 450
E | 433 | 546
F | 520 | 408
G | 624 | 135
H | 749 | 132
I | 899 | 91
Summary
With 70 times the polarization sensitivity of Planck, PICO will provide the next generation of full sky mm-wave observations. These data will allow the astronomical community to understand the universe across many scales from inflation and the growth of structure to galaxy evolution and star formation.
Scientific Observations
Measure or set upper limits on primordial B-modes with σ(r) ∼ 10-5
Determine the number of light relic particles, Neff, to σ(Neff) = 0.03
Measure τ, the optical depth to reionization to cosmic variance limits, σ(τ) = 0.002
  Along with DESI-BAO observations, measures Σmν, the sum of neutrino masses at ≥4σ
Map Galactic magnetic fields from large scales to 0.05 pc in 10 nearby molecular clouds
Discover 10,000s of protoclusters and clusters via the SZ effect
Map the CIB and dusty infrared galaxies across the full sky
1.2 m Cross Dragone
Larger, difficult to baffle sidelobes
f/2.5 or greater increases focal plane size and mass
Large secondary difficult to actively cool
Lower optical aberrations
[1] C. Dragone, "First-order correction of aberrations in Cassegrainian and Gregorian antennas," in IEEE Transactions on Antennas and Propagation, vol. 31, September 1983.
Mirrors at 40K, 4K, emissivity,
Active cooling of stop and secondary
Stop at 4K
FDM/TDM readout system, > x100 multiplexing
Lens coupled broadband multichroic pixels
Edge taper of 5,10,20 dB
100 mK bath
Psat = 2x Pload
4 year mission at 95 % observing efficiency
Orbit at L2
White noise: photon, phonon, readout, Johnson
Details. . . .
12,356 single polarization TES bolometers
Lens coupled tri-chroic pixels
FDM or TDM readout , > 100x multiplexing factor
White noise only
Includes photon (dominates), phonon, readout, and Johnson noise terms
4 year mission at 95% observing efficiency
Total integrated polarization map depth of 0.63 µKCMB arcmin
L2
Solar
illumination
Sun
Precession axis
Spin axis
Boresight
α
β
Sensitivity
Three color pixels, six polarization sensitive detectors per pixel
10 cm
50 cm
50 cm
1.2 m Cross Dragone
Larger, difficult to baffle sidelobes
f/2.5 or greater increases focal plane size and mass
Large secondary difficult to actively cool
Lower optical aberrations
0.5 m Open Dragone
Lower resolution
Physically smaller focal plane reduces detector count
Smaller system reduces costs
1University of Minnesota, Minneapolis, 2Princeton University, Princeton, 3Jet Propulsion Laboratory, Pasadena, 4Lawrence Berkeley National Laboratory, Berkeley, 5Villanova University, Villanova, 6Astroparticule et Cosmologie, Paris, 7University of Pennsylvania, Philadelphia, 8National Radio Astronomy Observatory, Charlottesville, 9University of California, San Diego, 10University of California, Davis, 11Goddard Space Flight Center, Greenbelt, 12University of Michigan, Ann Arbor †Email: kyoung@astro.umn.edu
Focal Plane,
100 mK
Secondary, 40 K
Aperture Stop, 40 K
Primary, 40 K
Reference
The PICO collaboration thanks the National Aeronautics and Space Administration (NASA) for supporting this study.
A
B
H
C
G
D
F
E
I
Replace this?